## Slide 1: More Specific Announcements in BGP
Geoff Huston
APNIC

## Slide 2: What’s a more specific?
A prefix advertisement that refines a “covering” advertisement
10.0.0.0/8
10.1.0.0/16

## Slide 3: Why advertise a more specific?
I: To redirect packets to a different network: “hole punching prefixes”
10.0.0.0/8
AS 65530
10.1.0.0/16 AS 138000
Different Origin AS

## Slide 4: Example: Type I
Network Path
>* 72.249.184.0/21 4777 2497 3356 36024
>* 72.249.184.0/24 4777 2497 2914 40824 394094

## Slide 5: Why advertise a more specific?
II: To redirect incoming traffic to different network paths: “traffic engineering prefixes”
10.0.0.0/8
AS 65530
10.0.0.0/9 AS 65530
10.128.0.0/9 AS 65530
AS 65536
AS 65537
Same Origin AS, different AS Path

## Slide 6: Example: Type II
Network Path
*> 1.37.0.0/16 4608 1221 4637 4775 i
*> 1.37.27.0/24 4608 1221 4637 4837 4775 i
*> 1.37.237.0/24 4608 1221 4637 4837 4775 i

## Slide 7: Why advertise a more specific?
III: To mitigate more specific prefix hijacking: “more specific overlays”
10.0.0.0/22 AS 65530
10.0.0.0/24 AS 65530
10.0.1.0/24 AS 65530
10.0.2.0/24 AS 65530
10.0.3.0/24 AS 65530
Same Origin AS, same AS Path

## Slide 8: Example: Type III
Network Path
*> 1.0.4.0/22 4608 4826 38803 56203 i
*> 1.0.4.0/24 4608 4826 38803 56203 i
*> 1.0.5.0/24 4608 4826 38803 56203 i
*> 1.0.6.0/24 4608 4826 38803 56203 i
*> 1.0.7.0/24 4608 4826 38803 56203 i

## Slide 9: How many eBGP route advertisements are more specifics?
AS 131072 – 13 October 2017
Routes Advertised Address Span
BGP Routes: 685,895 2.86B /32s
More Specifics: 365,022 (53%) 1.04B /32s (36%)

## Slide 10: How many eBGP route advertisements are more specifics?
AS 131072 – 13 October 2017
Routes Advertised Address Span
BGP Routes: 685,895 2.86B /32s
More Specifics: 365,022 (53%) 1.04B /32s (36%)
Over one half of the BGP routing table does not announce reachability to “new” destinations, but attempts to refine the way in which existing destinations can be reached

## Slide 11: Has this changed over time?
IPv4

## Slide 12: Has this changed over time?
IPv4
IPv6

## Slide 13: Has this changed over time?
IPv4
IPv6
Lets use the ratio of More-Specifics to the total route set

## Slide 14: Has this changed over time?
IPv4
IPv6
Oddly stable at 50%
Still growing
2007
2007
now
now

## Slide 15: More Specific Types – Prefix Counts
IPv4
IPv6

## Slide 16: More Specific Types – Relative Counts
IPv4
IPv6

## Slide 17: More Specific Types – Relative Counts
IPv4
IPv6
Hole Punching
Overlay

## Slide 18: More Specific Types
In both IPv4 and IPv6:
Type I prefixes (”hole punching”) are declining over time (relatively)
Type II prefixes (“traffic engineering”) have been relatively constant at some 30% of more specifics
Type III prefixes (“overlays”) have risen (relatively) and are now the more prevalent form of advertised more specifics

## Slide 19: What about Address Spans covered by more specifics?
IPv4
IPv6
Yes, this is a LOG scale

## Slide 20: What about Address Spans covered by more specifics?
IPv4
IPv6
Lets use the ratio of More-Specifics to the total address span

## Slide 21: What about Address Spans covered by more specifics?
IPv4
IPv6
Lets use the ratio of More-Specifics to the total address span
27%
2%

## Slide 22: Address Span: Breakdown into Types
IPv4
IPv6

## Slide 23: % of Total Span: Breakdown into Types
IPv4
IPv6
It’s mostly overlays!

## Slide 24: Overlays are the majority of More Specifics
The initial IPv6 network had little in the way of overlays and had a high proportion of Type I (Hole Punching) more specifics. This has changed over time and the recent profile is similar to IPv4
In both protocols the largest block of more specific announcements in terms of address span are “overlays” where the AS Path of the enclosing aggregate and the more specific are identical

## Slide 25: Overlays are the majority of More Specifics
Are Overlays “polluting” the BGP Space?
  Overlays do not change routing, but do these more specifics add to the routing load?

## Slide 26: Updates
Let’s look at “routing load” by looking at BGP updates
Our questions are:
  Are more specifics “noisier” than aggregates?
  and
  Are overlays more active in terms of BGP Updates than other prefixes?

## Slide 27: Update count by Prefix Type
IPv4
IPv6

## Slide 28: Update count by Prefix Type
IPv4
IPv6

## Slide 29: Update Count
In IPv4 the update count for more specific prefixes is greater than the comparable count for root prefixes, while the opposite is the case in IPv6.
But the relative count of more specifics is lower in IPv6
Let’s “normalise” this by dividing the update count by the number of prefixes to get the average update count per prefix of each type

## Slide 30: Relative Update count by Prefix Type
IPv4
IPv6

## Slide 31: Relative Updates
On average, in IPv4 More Specifics are slightly noisier than IPv4 Roots, while in IPv6 roots and more specifics are equally likely to be the subject of BGP updates
Are different types of more specifics more or less stable in BGP terms?

## Slide 32: Average Number of Updates Per More Specific Prefix Type
IPv4
IPv6

## Slide 33: Average Number of Updates Per More Specific Prefix Type
In IPv4 Type II Traffic Engineering Prefixes show a slightly higher level of BGP instability on average over Type I Hole Punching Prefixes, while Type III Overlay Prefixes show the highest levels of stability of more specifics
In IPv6 this has only been apparent in the past three years which Type II Traffic Engineering Prefixes showing the greatest levels of BGP instability , and Type I Hole Punching more specifics showing the highest levels of relative stability

## Slide 34: BGP Instability is heavily skewed
IPv4
IPv6

## Slide 35: What Type of Prefixes are more Unstable?
IPv4
IPv6

## Slide 36: What Type of Prefixes are more Unstable?
Type II More Specific Prefixes (Traffic Engineering) are approximately twice as likely to be unstable than either root prefixes or other types of More Specifics in both IPv4 and IPv6
This matches a rough intuition about the nature of more specifics, where overlays and hole punching would be expected to be as stable as root announcements

## Slide 37: Average Number of Updates per Active Prefix Type
IPv4
IPv6

## Slide 38: Average Number of Updates per Active Prefix Type
In IPv4 Type II Traffic Engineering Prefixes have a greater average number of updates than other prefix types
In IPv6 Root Prefixes tend to have a lower average number of updates than other prefix types
Perhaps the significant message here is that IPv6 has a higher inherent level of instability – unstable prefixes in IPv6 have 100x more instability events per unstable prefix on average than unstable prefixes in IPv4

## Slide 39: What if…
All Overlay more specific prefixes were removed from the routing table?

## Slide 40: Table Size Implications
IPv4
IPv6
-150,000
-10,000

## Slide 41: Update Count Implications
IPv4
IPv6

## Slide 42: What if…
All Overlay more specific prefixes were removed from the routing table?
Both IPv4 and IPv6 routing tables would drop in size by approximately 30%, as Overlay more specifics are now the predominate type of more specifics in the routing tables
The rate of dynamic instability in BGP would not change by any significant amount, as overly more specifics are relatively stable prefixes

## Slide 43: Summary of Findings
More specifics add to both the size and the update load of BGP
However BGP itself is both a reachability and a traffic engineering tool, and more specifics are often used to qualify reachability by traffic engineering. We have no other viable internet-wide traffic engineering tools, so this particular use of BGP really has no alternative
Recent years have seen the decline of hole punching as more providers tend to treat their address blocks as integral units.
Overlays are becoming more prevalent. While this has implications in terms of total table size it has no significant impact on BGP update rates.

## Slide 44: Summary of Findings
There is the question of total instability in IPv6 being far greater than IPv4, but this is not intrinsically an issue with more specifics, but a more general issue of BGP routing instability in IPv6
  More investigation called for!

## Slide 45
Thanks!